| Location / Sites: Various | Task / Activity: Rail Infrastructure Management | Equipment and plant |
| --- | --- | --- |

| Name: Matt Traynor | Position: Managing Director | Date: Jan 2022 | Ref No: RIM02 |
| --- | --- | --- | --- |

| No | Hazard Identification | Associated risks | Who & Number at risk | Existing control measures | Consequence | likelihood | Current risk rating | Additional controls | Consequence | likelihood | Post risk rate |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Damage to signal power supply cables | Possible damage to signalling circuit, non-detection, trains fail to stop, collision, derailment | All | Ensure sufficient/competent personnel are available | 4 | 2 | 8 | Sufficient number of men to task, official route, sufficient time, competence | 4 | 1 | 4 |
| 2 | Equipment/plant strike overhead line equipment | Electrocution, burns, fatality, fire/explosion, damage to equipment and property | All | Site safety rules. Not to work without isolation | 4 | 2 | 8 | Adhoc training /competence assessments Not to work without isolation | 4 | 1 | 4 |
| 3 | Equipment/plant strike live rail conductor | Electrocution, burns, fatality, fire/explosion, damage to equipment and property | All | Site safety rules. Not to work without isolation | 4 | 3 | 12 | Adhoc training /competence assessments Not to work without isolation | 4 | 2 | 8 |
| 4 | Equipment/plant strike track feeder | Electrocution, burns, fatality, fire/explosion, damage to equipment and property | All | Site safety rules. Not to work without isolation | 4 | 3 | 12 | Adhoc training /competence assessments Not to work without isolation | 4 | 2 | 8 |
| 5 | Equipment/plant strike sub-station feeder | Electrocution, burns, fatality, fire/explosion, damage to equipment and property | All | Site safety rules. Not to work without isolation | 4 | 3 | 12 | Adhoc training /competence assessments Not to work without isolation | 4 | 2 | 8 |
| 6 | Line presumed to be isolated, complacency, familiarity | Electrocution, burns, fatality, fire/explosion, damage to equipment and property | All | Site safety rules. Not to work without isolation | 4 | 3 | 12 | Adhoc training /competence assessments Not to work without isolation | 4 | 2 | 8 |

Matt Traynor

Managing Director

January 2022